## Slide 1: GIS (Geographic Information Systems) Applications in marketing Austin College April 2014
Dr. Ronald Briggs
Professor Emeritus
The University of Texas at Dallas
Program in Geospatial Information Sciences
briggs@utdallas.edu

## Slide 2: Overview
Geographic Information technologies
GIS data concepts
Applications
  In marketing
  In environmental studies (at noon)

## Slide 3: Geographic Information Technologies
GIS: one of three technologies which have revolutionized the handling of spatial or locational data, which is critical for marketing
Global Positioning Systems (GPS)
Remote Sensing (RS)
Geographic Information Systems (GIS)
.
Made it easy to do things which in the past had been time consuming, expensive, or even impossible

## Slide 4: Geographic Information Technologies
1. Global Positioning Systems (GPS)
  a system of earth-orbiting satellites which provide precise location on the earth’s surface
  GPS gave us exact locations inexpensively
  didn’t need an expensive surveyor

## Slide 5: Geographic Information Technologies
2. Remote Sensing (RS)
  collecting data without direct contact with the object being measured
  use of satellites or aircraft to capture information about the earth’s surface
  Expensive field surveys far less necessary
  Especially important for environmental applications

## Slide 6: Geographic Information Technologies
3. Geographic Information Systems (GIS)
  Software systems for input, storage, retrieval, analysis and display of geographic (spatial) information
gave us inexpensive map production/display and easier analysis
  don’t need a professional cartographer
  But still need analysts!
Input
Display
Analysis

## Slide 7: The Synergism of Three Technologies
  GPS and Remote Sensing provide data for GI Systems.
  GI Systems allow the effective use of GPS and RS data.
GPS data
RS data
GI Systems

## Slide 8: GIS data concepts

## Slide 9: Geographic Information System: intuitive description
A map with a database behind it
Which you can use:
to support on-going operations
  Where are my delivery vehicles now?
to make strategic decisions
  Where shall I locate my new store
to conduct scientific inquiry
  Are grocery prices higher in low income neighborhoods?

## Slide 10
Management Information Systems
and
Geographic Information Systems
What’s the difference?
In practice, they are becoming more and more the same, but lets look at the classic differnece

## Slide 11: The Uniqueness of GIS uses explicit location on earth’s surface to relate data
SS #
We all have Latitude and Longtitude !!
But I don’t have a SS # !!
Everything happens someplace. Is there anything more in common?
“Allows the integration of disparate data hitherto confined to separate domains”
--allows you to bring stuff together that you couldn’t before
--customer’s homes and store locations
--polluted rivers and factory locations

## Slide 12
The GIS Data Model:
A layer-cake of information
Each layer is a different phenomena
  elevation, streets, ownership parcels, land use
Layer are related based on common geographic coordinates
  Latitude & longitude or projected X,Y coordinates

## Slide 13
Real World
Vector Representation
Raster Representation
Two data types:
Vector and Raster
“raster is faster but vector is corrector”
line
polygon
point

## Slide 14: Representing Data with Raster and Vector Models
1. Raster Model
area is covered by grid of equal-sized, square cells (usually)
each cell given a single value based on the majority feature in the cell, such as land use type.
Multi-family
Single family
retail
industry
retail
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
2
2
2
2
2
2
2
3
3
3
2
2
2
2
2
2
2
3
3
3
2
2
2
2
2
2
2
3
3
3
2
2
4
4
2
2
2
3
3
3
2
2
4
4
2
2
2
3
3
3

## Slide 15: Representing Data with Raster and Vector Models
Raster Model
Great for some data such as elevation, rainfall, land use
  environmental data in general
Doesn’t work so well for others such as land ownership, streets,
  human data in general
Brown
Smith
Lee
Santos
Lee
0
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
1
1
1
1
1
4
4
5
5
5
2
2
2
2
2
2
2
3
3
3
2
2
2
2
2
2
2
3
3
3
2
2
2
2
2
2
2
3
3
3
2
2
4
4
2
2
2
3
3
3
2
2
4
4
2
2
2
3
3
3

## Slide 16: Representing Data with Raster and Vector Models
Vector Model
Features in the real work can be represented either as:
points (nodes): intersections, stores, homes, trees, poles, fire plugs, airports, cities
lines (arcs): streets, sewers, streams
areas (polygons): land parcels, voting precincts, cities, counties, forest, rock type
Birch
Cherry
I
II
III
IV
1
4
3
A35
Smith
Estate
A34
2
5
6
More complex, but more accurate and flexible

## Slide 17
Street Network layer: lines
Land Parcels layer: polygons
Raster layer (image)
Digital Ortho Photograph
Digital Ortho photo:
visual properties of a photograph with the positional accuracy of a map, in computer readable form.
2 vector
Layers
Example

## Slide 18
Overlay based on Common Geographic Location

## Slide 19
Parcels within a half mile buffer of Park and Central
Analysis
Data Table

## Slide 20: GIS in practice Marketing examples

## Slide 21: Real estate sales and prices Dallas area, year on year 1st Q 2014
Source: Dallas Morning News Friday April 18, 2014, p. 7D

## Slide 22
http://www.dallasnews.com/business/databases/20140417-area-home-sales.ece
Interactive database—click on Richardson

## Slide 23
MGIS: map with a database behind it

## Slide 24: Real estate sales and prices Dallas area, year on year 1st Q 2014 Color-coded or Choropleth map
Source: Dallas Morning News Friday April 18, 2014, p. 1D

## Slide 25: Real estate sales prices Analysis
Source: Dallas Morning News Friday April 18, 2014, p. 1D
Prices down cluster
21 Coppell
26 Irving
17 Oak Lawn
Prices up cluster
14 Oak Cliff
15 Southern Dallas
13 Southeast Dallas
4 Wilmer-Hutchins
Analysis: Why?

## Slide 26
Market Area Analysis using GIS for
Pottsboro Regional Library
Competitors
(other libraries)
Demographic Data
(potential market)
Data from ESRI, Inc. ArcGIS Business Analyst

## Slide 27
Information on competitors
GIS: map with a database behind it.

## Slide 28
Current customers: list derived from operational records

## Slide 29
Customers geocoded to their home address

## Slide 30
Location of library card holders, Pottsboro Area Public Library,
Overlay of city boundaries
November, 2013

## Slide 31
Demographic data on our market area:
--data by census block
--use to calculate market penetration

## Slide 32
Population in each census block group:
--need to add count of our customers

## Slide 33
Points in polygon operation
--counts the number of points falling in each polygon
--the number of customers in each block group
Achieved with a spatial join
--join points file to polygon file
Calculate market penetration
--now have population and count of customers for each block group we can calculate market penetration as:
Customer Count / Total Population*100

## Slide 34
MarkPen = Count (of customers)/2012 Total Population*100
Market Penetration calculated as:
Spatial join adds Count of customers for each polygon

## Slide 35
Creating a color coded (choropleth) map
for market penetration

## Slide 36
Market Penetration map

## Slide 37
73% is a remarkably successful market penetration!
96.697 33.797
Data problem! 657 patrons have only zip code for address
--all geocoded to same location

## Slide 38
657 patrons geocoded to here
(center point for 75076)
But could live anywhere in here (75076 zip code area)

## Slide 39
In God we trust, all others bring data.
Michael Bloomberg
In God we trust, all others bring good data.

## Slide 40
Voting sites reduced from 54 in 2010 to 36 in 2012 to 22 in 2013
  but could vote at any site in 2013
No analysis done
  Would this increase distances voters had to travel?
  Would it differentially impact minorities?

## Slide 41
Data for all census blocks in Grayson County (6,705) for total population, voting age population, and four racial/ethnic groups
Use GIS to calculate average travel distance to
  54 local precinct voting sites in 2010
  36 local precinct voting sites in 2012
  22 closest voting site (irrespective of precinct) in 2013

## Slide 42
Grayson County Texas | Average Travel Distance to Poling Sites |  |  |  |  | 
PANEL A Distance in miles | Total | 18 and Over |  |  |  | 
 | Population | Population | Hispanic | Anglo | AfAm | Mix & Other
Voting Sites 2012 (36) | 2.27 | 2.33 | 1.54 | 2.50 | 1.17 | 2.08
Voting Centers 2013 (22) | 2.20 | 2.24 | 1.51 | 2.39 | 1.26 | 2.06
PANEL B Change in miles |  |  |  |  |  | 
 | -0.07 | -0.08 | -0.03 | -0.10 | 0.09 | -0.02
PANEL C % Change |  |  |  |  |  | 
 | -3.2 | -3.6 | -2.1 | -4.2 | 7.8 | -1.1
Comparing results for 2012 (36 sites) when had to vote at your site,
to 2013 (22 sites) when vote at any site
  average travel distances went down (negative values for change)
  flexbility of going to any site offset the smaller number of sites (22 rather than 36)
African Americans the sole exception
  Travel distance increased by 7.8%
  But only 484 feet in absolute terms

## Slide 43: Thiessen (Voroni) polygons: --the area closer to a point than to any other point --a store’s “natural” trade area
Source: Jesse K. Pearson A Comparative Business Site-Location Feasibility Analysis using GIS Systems and the Gravity Model
Department of Resource Analysis, Saint Mary’s University of Minnesota, Minneapolis, MN

## Slide 44: Thiessen polygons: applications
Calculate customer potential in each area polygon
Do each of your stores have similar penetration
  Are there laggards?
consider new stores at intersection of polygons with large customer potential

## Slide 45: Drive-time analysis for store locations: commonly used to assess the potential of different possible sites

## Slide 46: Maximal coverage models
Given
A set of demand polygons (7)
A set of potential sites (9)
Where locate three facilities
to maximize sales (stores)
to minimize travel distance
(fire stations)
Source: Church and Murray 2008

## Slide 47
http://www.livescience.com/44622-beer-on-twitter-finding-drinking-patterns-in-tweet-data-infographic.html
Tweets sent between June 2012 and May 2013 were searched for keywords pertaining to beer. Geotagging allowed the tweets to be located on a map
Matthew Zook , et. al. "The Geography of Beer.” Department of Geography, University of Kentucky
GIS and Social Media

## Slide 48: Thank you for inviting me Questions?
briggs@utdallas.edu
www.utdallas.edu/~briggs
(under Presentations)

## Slide 49: Resources: books and papers
Richard L. Church, Alan T. Murray Business Site Selection, Location Analysis and GIS
Wiley InterScience On-line, ISBN: 9780470432761, 2008
Miller, F. GIS tutorial for marketing. Redlands, CA: ESRI Press, 2007
Miller, F. Getting to Know ESRI Business Analyst. Redlands, CA: ESRI Press, 2010
Pick, James B. Geo-Business: GIS in the Digital Organization. Wiley, 2008
Boyles, David. GIS means business, Redlands, CA: ESRI Press, 2002
Grant Thrall, Business Geography and New Real Estate Market Analysis (Oxford: Oxford University Press, 2002)
Shepherd, Ian D. H. From Geography Department to Business School: Strategies for Transplanting GIS Courses between Disciplines Journal of Geography in Higher Education, 2009, Vol.33(1), p.28-45
http://www.gis.smumn.edu/GradProjects/RingoL.pdf
Linder G. Ringo Utilizing GIS-Based Site Selection Analysis for Potential Customer Segmentation and Location Suitability Modeling to Determine a Suitable Location to Establish a Dunn Bros Coffee Franchise in the Twin Cities Metro, Minnesota
Department of Resource Analysis, Saint Mary’s University of Minnesota, Minneapolis MN

## Slide 50: Resources: on-line examples
http://www.gis.smumn.edu/GradProjects/RingoL.pdf
Linder G. Ringo Utilizing GIS-Based Site Selection Analysis for Potential Customer Segmentation and Location Suitability Modeling to Determine a Suitable Location to Establish a Dunn Bros Coffee Franchise in the Twin Cities Metro, Minnesota
Department of Resource Analysis, Saint Mary’s University of Minnesota, Minneapolis MN
http://www.gis.smumn.edu/GradProjects/PearsonJ.pdf
Jesse K. Pearson A Comparative Business Site-Location Feasibility Analysis using GIS Systems and the Gravity Model
Department of Resource Analysis, Saint Mary’s University of Minnesota, Minneapolis, MN