## Slide 1: Crash and Burn Ariane 5
Kristen Hieronymus
SYSM6309 Advanced Requirements Engineering
20130803

## Slide 2: Table of contents
The Rocket
The Payload
37 Seconds After Launch
Video
Root Cause Analysis
Result
Irony
Recommendations
Historical Context
Continuing Spin Story

## Slide 3: Ariane 5 Rocket
June 4, 1996 launch
European Space Agency rocket
$7Billion development cost
10 years development time

## Slide 4: Payload
“Cluster” payload
European Space Agency program, in cooperation with NASA
4 satellites on-board
To fly in tetrahedral formation
To study Earth’s magnetosphere

## Slide 5: 37 seconds after launch…
Rocket self-destructed

## Slide 6: video
http://en.wikipedia.org/wiki/Ariane_5
http://upload.wikimedia.org/wikipedia/commons/8/81/Ariane_5_10_2007.ogg

## Slide 7: Root cause analysis
Trying to put a 64-bit value in a 16-bit register caused an overflow condition, which led to…

## Slide 8: Root cause analysis 2
The guidance system shut down, which led to…

## Slide 9: Root cause analysis 3
The backup (identical) guidance system shutting down after encountering the same error, which led to…

## Slide 10: Root cause analysis 4
A diagnostic bit pattern being sent to the steering system, which the steering system interpreted as flight data from the guidance system, rather than an error code indicating it was shutting down, which led to…

## Slide 11: Root cause ANALYSIS 5
The steering system making an unnecessary and abrupt course correction of 20 degrees, which led to…

## Slide 12: Root cause analysis 6
Aerodynamic forces ripping off the boosters from the rocket, which led to…

## Slide 13: Root cause analysis 7
Self-destruction sequence for the rocket, which led to…

## Slide 14: result
Complete loss of the rocket and the four expensive, and uninsured satellites on-board

## Slide 15: irony
The system which produced the overflow was not needed on the Ariane 5!
Leftover from Ariane 4, due to reuse of entire subsystem (cost savings)
Different launch preparation sequence from Ariane 4
Velocity on Ariane 5 higher than Ariane 4

## Slide 16: More irony
Ariane 4 had requirement to not use more than 80% of memory
So, 4 variables had error protection code, but 3 others didn’t
Horizontal Bias (Velocity) variable was one which didn’t have protection code

## Slide 17: Recommendations - Requirements
Include trajectory in requirements
Include the diagnostic bit pattern in the Interface document
Change assumptions from “software never encounters an error, except due to CPU failure, so shutdown and failover” to “handle software exceptions in the code which encounters them”

## Slide 18: Recommendations - Requirements
Add requirement to shut down software which is not useful anymore at that phase of launch
Add requirement to include actual SRI – not just simulator – in system test

## Slide 19: Recommendations - Process
Review all flight software for implicit assumptions
Better communication among participants:
  Specification reviews
  Code reviews
  “Justification document” reviews
Maintenance of “justification documentation”

## Slide 20: Recommendations - Process
Requirement prioritization due to potential impact
Treat “reused” modules more carefully
  Review for assumptions about system context
  Include thorough interface tests, rather than treating as “previously verified”
  Include error conditions in interface tests, not just “happy path”

## Slide 21: Recommendations - CODE
Document assumptions clearly in code
Add error protection code to report “best estimate” rather than shutting down

## Slide 22: Historical Context
Military expenditures falling
Commercial use “exploding”
Internationalization of competition for business
Aerospace responsible for 5% of France’s economy

## Slide 23: On-going spin story
Wikipedia lists as a “test launch”
Test launches do not carry expensive payloads

## Slide 24: Links
http://ec.europa.eu/enterprise/sectors/aerospace/files/aerospace_studies/aerospace_study_en.pdf
http://www.yale.edu/ynhti/curriculum/units/1990/7/90.07.06.x.html
http://cahiersdugres.u-bordeaux4.fr/2006/2006-15.pdf
http://www.around.com/ariane.html
http://en.wikipedia.org/wiki/Ariane_5
http://en.wikipedia.org/wiki/Cluster_mission
http://www.ima.umn.edu/~arnold/disasters/ariane5rep.html