## Slide 1: Embedded Programming and Robotics
Lesson 19
Raspberry Pi Programming in C

## Slide 2: Get the WiringPi Library
sudo apt-get install git-core
git clone git://git.drogon.net/wiringPi
Build the library:
cd wiringPi
./build

## Slide 3: Compiling C Programs
You can use any text editor, such as leafpad, nano, vi, etc. to create your source file
Always give the file a .c (lower case) extension, such as RobotControl.c
To compile to an executable, do this:
gcc –o RobotControl RobotControl.c
The –o option gives the output executable name

## Slide 4: Compiling C Programs
The parameter is the C file name, and the extension is required
If you get error messages about libraries not being found, use the sudo ldconfig command to check what default libraries are available

## Slide 5: Executing Your Program
Run the program with ./RobotControl
If you know about make files and shell scripts you can use them, but they’re beyond the scope of this simple introduction

## Slide 6: Writing a C Program
You’ll need to include the following two things:
#include <stdio.h>
#include <wiringPi.h>
They’re not needed on the Arduino, but you need them for C
The gcc compiler really compiles C++

## Slide 7: Writing a C Program
Initialize the library with the following:
wiringPiSetupGpio();
Set GPIO pins:
pinMode(LED1, OUTPUT);

## Slide 8: Writing a C Program
Blink an LED:
digitalWrite (LED1, HIGH) ;
delay (500) ;
digitalWrite (LED1, LOW) ;
delay (500) ;