## Slide 1: Embedded Programming and Robotics
Lesson 4
Sensors

## Slide 2: Digital Sensors
As we discussed before, many sensors are digital: on or off
This includes things like switches, motion sensors, etc.
Passive sensors, ones that don’t take power, or usually wired up the way you were shown in Lesson 3
Active sensors, such as motion detection, are wired as shown on the next slide. It’s called passive IR because it doesn’t emit anything, just detects it.

## Slide 3: Motion Sensor
Connect jumpers to the three pins of the PIR (Passive Infrared) motion sensor
Connect the vcc pin to the +5 on the prototype board
Connect gnd to ground on the prototype board
Connect out to pin 3 of your Arduino

## Slide 4: Motion Sensor
Back of the IR motion sensor
The middle pin, Digital Out, connect to an Arduino digital input pin

## Slide 5: Motion Sensor
Write code to read the sensor:
If the sensor reads 1, write HIGH to the LED pin
If it reads 0, write LOW to the LED pin

## Slide 6: Infrared Reflective Sensor
TCRT5000 Infrared Reflective Photoelectric Sensor used to detect lines
Can be used to make your robot follow a specific path
Used in the edge-follower robot

## Slide 7: Infrared Reflective Sensor
Connect vcc and gnd to +5 and ground, respectively
Connect A0 on the TCRT5000 to an analog input pin on the Arduino
Use analogRead to read from the sensor.
The larger the number, the further away

## Slide 8: Edge-Follower Program